## Slide 1
Revolutionizing Traffic Flow - Using Traffic Signal Performance Measures without Traditional Detection Methods
Steve Remias
Steve.Remias@INRIX.com
Notes: Introduce Yourself
Today were going to talk a problem that most everyone experiences and contributes to, but very little realize they do.

## Slide 2: Agenda
Why Are Signal Performance Measures (SPMs) Important?
Overview & Contrast Controller/Sensor-Based SPMs and GPS-Based SPMs
Use Cases
Notes: Session Goals are to:
Develop a Base-Level Understanding of SPMs
How to Get Started with SPMs – controller-based and/or GPS-based
Share Example Agency Story around both sensor based and GPS based SPMs

## Slide 3: The Opportunity
Poorly Timed Traffic Signals are Difficult to Manage
How Would We Know?
Wait for a phone call
Scheduled signal retiming
What Could We Do?
Install detection infrastructure
Manual data collection
Model with software
Hire a consultant
Why Should We Care?
Delay
> 330 mil. vehicle hours of delay per year at signals
Fuel Use
6 to 9% fuel savings at well timed signals
Emissions
1 gallon of fuel = ~20 pounds of CO2
Safety
Better managed signals = safer signals
Notes: Poorly Timed Traffic Signals
Let’s consider this urban signal in Charlotte (click)
A pretty standard 4 legged intersection (click) in a downtown urban core (click)
If there were a problem at this intersection, how would we know? (click)
If we knew about the problem, What could we do? (click)
Why should we care (click)
Read and elaborate on stats (click)

## Slide 4: These Solutions Don’t Scale
One intersection is easy. An entire network…..
The Solution
Use Data from Vehicles
Notes: An engineer managing one signal is relatively easy. Perform a traffic study, retime the signal, observe the benefits (click)
An engineer managing an entire network of signals becomes more difficult, time consuming, and expensive.
How can I identify the signals I should be prioritizing (click)
Our solution is leveraging the vehicles with in-dash GPS devices to give us an idea of how signalized intersections are performing (click)
As vehicles move through the network when they pass through a signalized intersection we can leverage those waypoints to tell us how an intersection is performing (click)

## Slide 5: Current Practice
Hire Consultant
Data Collection
Modeling
Results
Source: jamartech.com
Source: trafficware.com
Implement
Develop Guidelines
How do we know how well we did?
How do we know where we should do this?
How do we know if we collected the right data?

## Slide 6: What are Automated Traffic Signal Performance Measures?
Detector-Based

## Slide 7: What are Signal Performance Measures?
Examples:
Observed metrics at a signalized intersection that can be used to measure agency objectives
Travel Time
Approach Speed
Split Failures
Turn Ratios
Vehicle Counts
Control Delay
Stops / AOG
Level of Service
Coordination
Pedestrian Delay
Phase Termination
Yellow/Red Actuations
Splits
Left Turn Gap Acceptance
Preemption Count

## Slide 8: Performance Measures for Traffic Signal Systems
https://docs.lib.purdue.edu/cgi/viewcontent.cgi?article=1002&context=jtrpaffdocs
Split Failure Monitor
Purdue Coordination Diagram
Approach Delay
Volume
Notes: Steve to add text and edit slide as desired.

## Slide 9: UDOT Open Source ATSPM Platform
https://udottraffic.utah.gov/ATSPM

## Slide 10: What are agencies using them for?
Source: Kittelson & Associates Inc. & Purdue University “NCHRP Project 03-122: Performance-Based Management of Traffic Signals” January 2017

## Slide 11
Image: Chevy

## Slide 12: GPS Based Signal Performance Measures
Metrics for each vehicle
Travel Time
Approach Speed
Vehicle Stop
Vehicle Double Stop
Movement (Left, Thru, Right)
DISTANCE
TIME
Arrival
Departure

## Slide 13: The Metrics – Assumptions
DISTANCE
TIME
42 sec
ARRIVAL ON GREEN
DISTANCE
TIME
61 sec
ARRIVAL ON RED
DISTANCE
TIME
100 sec
SPLIT FAILURE
1
2
3

## Slide 14: Developing the Metrics
14
NB
Inbound Length
Outbound Length
Travel Time
Speed
Reference Travel Time
Delay
150m
5th Percentile
Time
Distance
Stop <6 mph
14
80 m

## Slide 15: Real Trajectory Data

## Slide 16: Derive Insights from the Vehicles Themselves
Signal Performance Metrics Available
Travel Time
Approach Speed
Split Failures
Turn Ratios
Vehicle Counts
Control Delay
Stops / AOG
Level of Service
DISTANCE
TIME
Notes: From the waypoints we can derive performance measures like……
At every intersection, everywhere, all the time (click)
We aggregate all of those metrics into our product INRIX Signal Analytics
The product allows you to identify underperforming intersections, compare intersections before and after retiming projects, rank intersections based on any of the metrics and most importantly scale (click)

## Slide 17
Notes: INRIX Signal analytics can be turned on at any of the 240,000+ intersections currently available in the platform or any other intersection that is identified by an agency or DOT. (click)
The basis for this platform is a suite of cloud based services from Amazon Web Services.
The cloud allows billions of data points to be turned into actionable insights for agencies to save time, fuel, and reduce the emissions caused by poor traffic signal timings. (click)

## Slide 18: Sensor-Based / Detector-Based SPMs
Strengths
~100% of traffic
Includes signal timing information
Includes phase termination
Visualize detector actuations
Limitations
Complex detector layout
System-wide comparison difficult
Many points of failure
Some metrics are approximated
Notes: Opportunities
  All to nearly all traffic captured (depending on sensor/detector layout)
  Direct measure of cycle length, splits, offsets, pedestrian/bike/transit/truck/EV phasing
  Know phase termination... omit, skip, gap-out, max-out, force-off, coordination
  See detector actuations (depending on sensor/detector layout)
Limitations
  Relies on more complex detector/sensor layout & configuration
  Inconsistencies in detector/sensor layout or functionality can make SPM eval/compare difficult or inaccurate
  Introduces more points of failure
  Approximates SPMs like AOG/AOR, Split Fails, Delay rather than directly measuring

## Slide 19: GPS, Trajectory-Based SPMs
Strengths
Real ‘observed’ vehicles
No added infrastructure
Scale & Consistency
Integrated Software
Limitations
Only a sample of vehicles
No direct signal/phasing measurement
Vehicle only
Not in real time
Notes: Opportunities
  Real Road User Trajectories --> Accurate SPMs
  GPS-vehicle to cloud --> No agency infrastructure or extra components to purchase/maintain
  Integrated SPM analytics calculation software --> easy, simple SPM analysis
  Easy to scale to network level for agency-wide relative comparisons
  Probe sample size is increasing exponentially
  Historical Data back to January 2020 (INRIX Signal Analytics)
  Limitations
  Is based on probe data --> only a sample of conditions
  No direct signal phasing/timing measurement
  Vehicle only, currently

## Slide 20: Use Case - Washington County – Customer Complaint Response
I-5
Sagert
“Around 4pm major back-ups on 65th near Meridian Park Hospital… takes me longer to get from I-5 to Sagert (0.9 mi) than from Beaverton to I-5 Nyberg exit (~ 8 miles)…
Please look at the signal lights…”
– concerned citizen phone call
Customer Complaint
Notes: Washington County, OR used the tool to investigate a customer complaint.
Essentially a 1 mile stretch of road was taking longer to travel than an 8 mile stretch of roadway as a result of a traffic signal.
A customer reported the issue and INRIX Signal Analytics was used to investigate.

## Slide 21: Use Case #3 Washington County Customer Complaint Response
Before Adjustment
After Adjustment
Notes: Upon investigation a problem was apparent in the IQ dashboard. The SB movement experiences significant delay and split failures at the intersection. After adjusting the intersection and some parameters in the cabinet. The result was an improvement in both the control delay and a reduction in split failures during the PM peak period.

## Slide 22: Washington County Energy Calculator Example
Before Adjustment
After Adjustment
Using the energy metric calculator on the previous Washington County example, there would be a projected annual savings of:
Over 2,195 gallons of fuel saved
Over 22 tons of carbon dioxide equivalents
Energy Savings

## Slide 23
Steve Remias
Steve.Remias@inrix.com
Thank you!
INRIX SIGNAL ANALYTICS